## Slide 1: Logic And Computers
Gates and stuff

## Slide 2: Objectives
Learn about some people who had a significant impact on computer operations
Develop a basic understanding of how binary numbers are represented and added in a computer
Learn about logic gates and truth tables.

## Slide 3: Where it all started
George Boole
  George Boole – 1850's
  English Mathematician
  Created algebra of logic now known as Boolean Algebra
  Uses True or False
Claude Shannon
  Claude Shannon 1930's
  Applies Boolean algebra to electronic circuits
Binary digits can be represented by mechanical relays, vacuum tubes or transistors.
  On
  Off
  Represented by binary numbers 0 and 1

## Slide 4: History of Computer Operations
An early byte 1950's:
http://mason.gmu.edu/~montecin/vacuum_tube.html

## Slide 5: History of Computer Operations
Transistor – invented in 1947 Bell Labs
Replaced the vacuum tube
Acts as a switch or gate – can store a bit of 0 or 1
http://www.protostack.com/transistors

## Slide 6: History of Computer Operations
Volatile
Need to temporarily store information such as 0's and 1's – done in RAM
Need to perform operations in processor
A bus is used to move bits from processor to RAM
Disappears when electricity is turned off
Non-Volatile
Need to store information more permanently
Hard drive
Flash Memory Devices – "Stick" or USB Drive
Uses different technology than RAM

## Slide 7: History of Computer Operations
Integrated Circuits
  Operate according to Boolean algebra and consists of a series of gates
  Modern computers can integrated circuits with millions of transistors
http://geekyginger.com/integrated-circuits-soul-of-your-you-device/
http://imgkid.com/integrated-circuit.shtml

## Slide 8: Basics of Circuits
Computer circuits are made up of gates. Typically, there are three main types of gates
  AND Gate
  OR Gate
  NOT Gate
In addition there are
  NAND Gates
  NOR Gates
  XOR Gates

## Slide 9: Basics of Circuits
AND Gate
Symbol
Truth Table for AND Gate
Lets Make One: http://www.neuroproductions.be/logic-lab/
INPUT A | INPUT B | OUTPUT AB
T | T | T
T | F | F
F | T | F
F | F | F
http://www.ee.surrey.ac.uk/Projects/CAL/digital-logic/gatesfunc/index.html#introduction

## Slide 10: Basics of Circuits
EXOR Gate Exclusive OR
Symbol
Truth Table for AND Gate
Lets Make One: http://www.neuroproductions.be/logic-lab/
INPUT A | INPUT B | OUTPUT
T | T | F
T | F | T
F | T | T
F | F | F
http://www.ee.surrey.ac.uk/Projects/CAL/digital-logic/gatesfunc/index.html#introduction

## Slide 11: Adding Binary Numbers
Rules:
0 + 0 =0
0 + 1 = 1
1 + 0 = 1
1 +1 = 10 the 1 is a carry
1 + 1 +1= 11 the first 1 is a carry
Remember in Base 10 when you add 9 + 1 you get 0 and carry the one
Same is true in binary. When you add 1 + 1 you get 0 and carry the one

## Slide 12: Adding binary numbers
Ex:
00 01
01 01
01 10 here we carry the 1 to the 2's column
011
011
Here we carry a 1 to the 2's column and then add
1 + 1 +1 to get 1 and then carry a 1 to the 4's
column – check your answer by converting to
Base 10: 0112 = 310 3 + 3 =6 and 1102 = 610

## Slide 13: Adding Binary Numbers
Half Adder Circuit
A | B | Output XOR - SUM | Output AND - CARRY
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Lets Make One: http://www.neuroproductions.be/logic-lab

## Slide 14: Basics of Circuits
OR Gate
Symbol
Truth Table for AND Gate
Lets Make One: http://www.neuroproductions.be/logic
lab/
INPUT A | INPUT B | OUTPUT A+B
T | T | T
T | F | T
F | T | T
F | F | F
http://www.ee.surrey.ac.uk/Projects/CAL/digital-logic/gatesfunc/index.html#introduction

## Slide 15: Basics of Circuits
Not Gate
Symbol
Truth Table for AND Gate
Lets Make One: http://www.neuroproductions.be/logic-lab/
INPUT A | OUTPUT
T | F
F | T
http://www.ee.surrey.ac.uk/Projects/CAL/digital-logic/gatesfunc/index.html#introduction

## Slide 16: Basics of Circuits
NAND Gate
Symbol
Truth Table for AND Gate
Lets Make One: http://www.neuroproductions.be/logic-lab/
INPUT A | INPUT B | OUTPUT
T | T | F
T | F | T
F | T | T
F | F | T
http://www.ee.surrey.ac.uk/Projects/CAL/digital-logic/gatesfunc/index.html#introduction

## Slide 17: Basics of Circuits
Full Adder
This circuit has three inputs – one for a carry.
https://asicdigitaldesign.wordpress.com/2007/05/23/aclp-2-solution

## Slide 18: Basics of Circuits
Typically a T = True and also would be represented by a 1
Typically a F = False and would be represented by a 0
Electricity:
  T = 1 = Circuit is ON
  F = 0 = Circuit is OFF
So, when solving a logic problem you want to think of a circuit being activated and turning on a light or bell as using a 1.
And, a circuit that has no electricity flowing would be a 0
So, you want to represent action or danger with a 1: Turning on a sensor or an alarm.

## Slide 19: In Class Problem
Problem 1: Imagine a toxic waster incinerator.
Write a logic circuit and truth table with input A and Input B and Output Y where Y is 1 (produces signal and turns off waste inlet)only if both sensors show no flame.
Adapted from http://www.allaboutcircuits.com/vol_4/chpt_7/9.html
Sensor A detects no flame and sends an electrical signal noted as a 1
Sensor B detects no flame and sends an electrical signal noted as 1

## Slide 20: In Class Problem
Answer
Big Truth Table
So, The AND gate would work. It produces a 1 (signal) only if both A and B are signaling (1's)activating the alarm.
See illustration : http://www.neuroproductions.be/logic-lab/index.php?id=35172
Input A | Input B | AND | XOR | OR | NAND | NOT
0 | 0 | 0 | 0 | 0 | 1 | If 0
0 | 1 | 0 | 1 | 1 | 1 | Then 1
1 | 0 | 0 | 1 | 1 | 1 | If 1
1 | 1 | 1 | 0 | 1 | 0 | Then 0

## Slide 21: In Class Problem
Problem 2: Same toxic waste incinerator
  Create a circuit and truth table so that the Output Y (turns off waste inlet)if either one of the sensors show the flame is off.
  So flame off – danger - and sensor would activate and register a 1
  And a 1 going to the alarm would activate it.
  So, turn off if either sensor produces a 1 and also if both produce a 1
  http://www.neuroproductions.be/logic-lab/index.php?id=35173
Input A | Input B | AND | XOR | OR | NAND | NOT
0 | 0 | 0 | 0 | 0 | 1 | If 0
0 | 1 | 0 | 1 | 1 | 1 | Then 1
1 | 0 | 0 | 1 | 1 | 1 | If 1
1 | 1 | 1 | 0 | 1 | 0 | Then 0

## Slide 22: In Class Problem
Problem 3
Imagine there are two valves that pour a chemical into a vat. You never want to have both valves open at the same time. So if Valve A is open you want B closed and if Valve B is open you want Valve A closed. Draw a circuit with sensors and input that will have an output light that turns on and warns you if the system has failed. So, the alarm should go off if both valves are open.
So here you want either sensor to produce a 1 if its valve is open. And, if both sensors produce a 1 which means they are both open then the output of that is a 1 which turns on the light alarm. What if both valves are closed – then that is okay.
See next slide

## Slide 23: Summary
So when solving a word problem it helps to state what your 0 and 1's represent.
Example: When a sensor detects a loss of flame it generates a 1( the electricity is turned on)
Typically a 1 is turning the electricity on or activating something like an alarm.
You could say well, the sensor doesn't read any flame so therefore a 0 signal is generated but I think that is confusing. Let's stay with activation of a sensor or alarm =1.